Bearing

Have you ever wondered how things like inline skate wheels and electric motors spin so smoothly and quietly? The answer can be found in a neat little machine called a bearing.

The Basics
The concept behind a bearing is very simple: Things roll better than they slide. The wheels on your car are like big bearings. If you had something like skis instead of wheels, your car would be a lot more difficult to push down the road. That is because when things slide, the friction between them causes a force that tends to slow them down. But if the two surfaces can roll over each other, the friction is greatly reduced.

Bearing Loads
Bearings typically have to deal with two kinds of loading, radial and thrust. Depending on where the bearing is being used, it may see all radial loading, all thrust loading or a combination of both.

The bearings that support the shafts of motors and pulleys are subject to a radial load.

The bearings in the electric motor and the pulley pictured above face only a radial load. In this case, most of the load comes from the tension in the belt connecting the two pulleys.

The bearing above is like the one in a barstool. It is loaded purely in thrust, and the entire load comes from the weight of the person sitting on the stool.

Types of Bearings
There are many types of bearings, each used for different purposes. These include ball bearings, roller bearings, ball thrust bearings, roller thrust bearings and tapered roller thrust bearings.

Ball bearings, as shown below, are probably the most common type of bearing. They are found in everything from inline skates to hard drives. These bearings can handle both radial and thrust loads, and are usually found in applications where the load is relatively small.

In a ball bearing, the load is transmitted from the outer race to the ball, and from the ball to the inner race. Since the ball is a sphere, it only contacts the inner and outer race at a very small point, which helps it spin very smoothly. But it also means that there is not very much contact area holding that load, so if the bearing is overloaded, the balls can deform or squish, ruining the bearing.

Roller Bearings
Roller bearings like the one illustrated below are used in applications like conveyer belt rollers, where they must hold heavy radial loads. In these bearings, the roller is a cylinder, so the contact between the inner and outer race is not a point but a line. This spreads the load out over a larger area, allowing the bearing to handle much greater loads than a ball bearing. However, this type of bearing is not designed to handle much thrust loading.

A variation of this type of bearing, called a needle bearing, uses cylinders with a very small diameter. This allows the bearing to fit into tight places.

Ball Thrust Bearing
Ball thrust bearings like the one shown below are mostly used for low-speed applications and cannot handle much radial load. Barstools and Lazy Susan turntables use this type of bearing.

Roller Thrust Bearing
Roller thrust bearings like the one illustrated below can support large thrust loads. They are often found in gearsets like car transmissions between gears, and between the housing and the rotating shafts. The helical gears used in most transmissions have angled teeth -- this causes a thrust load that must be supported by a bearing.

Tapered Roller Bearings
Tapered roller bearings can support large radial and large thrust loads.

Tapered roller bearings are used in car hubs, where they are usually mounted in pairs facing opposite directions so that they can handle thrust in both directions.